LCD DISPLAY:

- main function：

- six function keys: 【TIME】、【+/RF】、【-/RCC】、【ALARM】、【MEM/12-24H】、【SN/LIGHT】

- four digits display hours, minutes, respectively

- Weather forecast function: 【Sun】, 【Sun + cloud】, 【cloud】, 【cloud + light Rain】or【 Cloud + light  Snow】；【cloud + heavy rain】 or【cloud + heavy Snow】

- Month Day week show

- Toggle Display Alarm Time

- Indoor Ambient Temperature:--9.9℃～50℃ [14.2℉～122℉]

- Outdoor Ambient temperature:--40℃ +70℃ [-40℉～158℉]

- Atomic  Automatic Clock Reception  (DCF/MSF/WWVB).

- Noisy and Sleepy function,5 minutes delay Noisy

- L LED backlight, delay of ten seconds

- Power on & reset

on the power or reset,LCD display 3 seconds, backlight at the same time lit ten seconds → buzzer BI a sound, → Press 【SN/LIGHT】 Enter the national region selection → check indoor temperature → into the normal state → into the RF receiver → into the RCC receive。

[Power On this product requires the user to first select Set Country region:  DCF= European EU; MSF = English UK;  WWVB= United States US, or go to setup mode to select Country area, when no signal is received in the area, automatically loops in three zones . signal will base on the last time you receive ]

[Select the interface in the national area, press [SN/LIGHT] button to switch selection,, confirm by any other key, if not, then the default is DCF European EU] ]

On power default Perpetual calendar display:

|  | Show time | Month / Day | Date | default language | Temperature unit | RCC | ZONE | ALARM Time |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DCF European version EU | 00:00:00 ( 24 Hour system ) | D/M | 2018 year 1 months 1 days, | German | ℃ | ON | 0 | 7:00AM |
| MSF British version UK | 12:00am ( Hour system) | D/M | 2018 year 1 months 1 days, | English | ℃ | ON | 0 | 7:00AM |
| WWVB US version US | 12:00am ( Hour system) | M/D | 2018 year 1 months 1 days, | English | ℉ | ON, DST ON | EST | 7:00AM |

- operation and display：

  - key Function：【TIME】、【+/RF】、【-/RCC】、【ALARM】、【MEM/12-24H】、【SN/LIGHT】

|  |  | 【TIME】 | 【+/RF】 | 【-/RCC】 | 【ALARM】 | 【MEM/12-24H】 |
| --- | --- | --- | --- | --- | --- | --- |
| Standard mode | Single Press | ------ | Switch alarm | c/f Convert | View Alarm | 12-24h Toggle |
|  | Long Press | Enter Time setting | Enter the RF registration mode | Manually enter the RCC receive mode | Enter Alarm Set | Clears the current maximum minimum value |
| Set mode | Single Press | Set Mode selection Setup Item | Set Single Step increment | Set Single Step decrement | Set Mode selection Setup Item | ------ |
|  | Long Press | ------ | Set 8 step / second increment | Set 8 Step / sec Decrement | ------ | ------ |

【SN/LIGHT】：battery-powered backlight key Point Light backlight 10 seconds, fire cattle power supply weak light switching

  - Key action：

- Long press the 【-/RCC】 key to begin the RCC receive and receive process Long Press 【-/RCC】 to exit the RCC receive

- Long Press 【TIME】 key, the buzzer BI , enter the setting

- Single Press【+/RF】 switch Alarm clock

- Switch temperature unit by 【-/RCC】 ℃/℉

- Single Press 【MEM/12-24H】 switch time format, 12H/24H  toggle

- Temperature Unit ℃/℉

- Click the 【ALARM】 button, switch to the alarm clock time display, and then press This key or no key switch back to the time display

- 【SN/LIGHT】 key , battery powered back Light key Point Light backlight ten seconds, fire ox power supply weak light switch

- when the alarm clock is ringing, press any key to stop the noise, press 【SN/LIGHT】key , into the sleepy state, will be delayed for 5 minutes Noisy

  - Time setting:

- Long Press 【TIME】 key >2 seconds, buzzer BI , enter time setting

- set order：

| Set Order | CY | ZONE |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DCF European Union | Country → | Time zone → | Years → | DM/MD → | Month → | Day → | Language → | Hours → | Min → | Exit |  |
| MSF British edition UK | Country → | Time zone → | Years → | DM/MD → | Month → | Day → | Language → | Hours → | Minutes → | Exit |  |
| WWVB US version US | Country → | ----- | Years → | DM/MD → | Month → | Day → | Language → | Hours → | Minutes → | DST On/off → | Exit |

- the setting range of the year 2000~ 2099

- the week changes with the day of the month

- set minute seconds to zero

- When setting, the item being set will blink at the 1HZ frequency

- Single press【TIME】Key, determine the setting result and goes to the next setup item

- Press 【+/RF】key, the Setting  item forward one step, and hold down 2 seconds, to advance at the 8 steps per second

- Press【-/RCC】key, the Setting  item back one step, and hold down 2 seconds to rewind at the 8 steps per second

- No settings in 20 seconds will save settings and exit

- Time Zone Description:

| DCF European Union time zone : | +-12H |
| --- | --- |
| MSFUK time zone : | +-12H |
| WWVB US version time zone [ 4 ] : | Eastern–est (GMT-5) |
|  | CENTRAL–CST (GMT-6) |
|  | Mountain–mst (GMT-7) |
|  | Pacific–pst (GMT-8) |

Language of the 5 languages correspond to:

| Language | English | Referred | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday | Sunday |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| United Kingdom | English | En | MON | TUE | WED | THU | FRI | Sat | SUN |
| France | French | FR | LUNs | MAR | MER | Jeu | VEN | SAM | DIM |
| Germany | German | GE | MON | DIE | MIT | DON | FRE | SAM | SON |
| Italy | Italian | IT | LUNs | MAR | MER | GIO | VEN | Sab | Dom |
| Spain | Spanish | Sp | LUNs | MAR | Mie | Jue | Vie | Sab | Dom |

  - Alarm Settings:：

- Long Press 【ALARM】 key, beep BI , enter alarm time set

- When setting, the item being set will blink at the 1HZ frequency

- Single press【【ALARM】Key, determine the setting result and goes to the next setup item

- Press 【+/RF】key, the Setting  item forward one step, and hold down 2 seconds, to advance at the 8 steps per second

- Press【-/RCC】key, the Setting  item back one step, and hold down 2 seconds to rewind at the 8 steps per second

- No settings in 20 seconds will save settings and exit

- after setting, if the time is not the key to exit the settings to return to the settings before the display, set up Alarm Clock opens naturally

- Single Press 【+/RF】switch Alarm clock

  - LED Light backlight Condition:

- Adapter  power supply，

  - after the power or RESET , LED high lighting

  - Press【SN/LIGHT】, the light in strong → weak → off，toggle  switch.

  - Even in a weak or off state, press except 【SN/LIGHT】  key LED to high light 10 seconds, then return  to the Previous state

  - The LEDs highlight  10 seconds, even when they are in a weak or inactivated state , and then return to the previous state

- DC Battery power supply

  - after the power or RESET , LED high lighting   10 seconds，then off

  - Press【SN/LIGHT】, LED high lighting   10 seconds，then off

  - Even in the off  state，press except 【SN/LIGHT】  key ,LED to high light 10 seconds, then  off

  - Off state the alarm sound，LED to high light 10 seconds, then  off

- function and effect description

  - Atomic RCC Function.

- Enters RCC receive condition：

  - Power On or reset select the country zone【DCF= European EU；MSF = English UK；WWVB= US】 Enter RCC receive

  - Long Press【-/RCC】Key to force the RCC to receive

  - In the receive process, single press【-/RCC】 key to stop RCC receive

  - only snooze key is available during the receive process, if want to press any other keys, you need to exit RCC receive status .

- RCC receive , traveling clock version description that the RCC signal receives based on the country region that is set by the user, switching sequentially between DCF→MSF→wwvb . For example: The last time you received a successful WWVB format, the next time you turn on RCC reception takes precedence over WWVB 's RCC Radio wave format

- RCC receive time 4-10 minutes

- RCC Receive graphics：

- sign flashing when received

- if receive successful , the entire RCC symbol will be full displayed;

- if receive signal not succeed ,the symbol disappeared and exit RCC ﹒

- Any non-set mode, long press【-/RCC】 Key, enter RCC manual Receive mode, and then press【-/RCC】key ,can stop the RCC receive

- WWVB US version US time [ Zone [ 4 ], Press "-/RCC" to switch during the RCC receive process PMCE four time zones

- Automatically receive the airwaves on every day of the night 1:03,2:03,3:03,4:03,5:03 ; every day 1:03,2:03 and 3:03 Force automatic reception,4:03 and 5:03 select receive, maximum receive

time is 12 minutes  , the receiver is automatically stopped if the correct time is not received within the specified time。

  - RF function：

- When the battery is installed , after the temperature and humidity are detected, automatically enter the RF receive 3 minutes

- Press the【+/RF】key in standard mode to force clear the data for the outdoor channel and Re-register

Outdoor data does not receive valid data within 60 minutes and automatically register

- When the temperature is lost, the signal is received again and the recovery temperature is displayed

  - Alarm function：

- Alarm Time 2 minutes

- Alarm format:0-20 sec, Bi Bi twice per second,21-40 seconds, per second Bi Bi Bi BI-tone 4 times ;41-120 seconds, continuous BI sounds

- When the alarm is ringing, press the 【SN/LIGHT】 key, will delay alarm 5 minutes, press the other keys to exit the alarm.

  - Temperature and humidity functions：

- Temperature Detection range:-9.9℃ ~50 ℃ [14.2℉~122℉ ] , higher than 50℃ display HH. H, less than -9.9℃ display LL.L

- Temperature and humidity detection cycle : 60 sec

- Temperature Precision range：20℃～30℃，±1.5℃；Other intervals is ±2℃

- Pause temperature and humidity detection when alarm is ringing or RCC reception is in progress

  - Weather forecast function：Sun；Sun + cloud；cloud；cloud + Rain【cloud +heavy Rain】；cloud + Snow【cloud +heavy Snow】

- Work Parameters :

| Project | Unit | MIN | TYPE | MAX |
| --- | --- | --- | --- | --- |
| Operating voltage | V | 2.4 | 3.0 | 3.5 |
| Static current | uA | -- | -- | 30 |
| Operating temperature | ℃ | -10 | -- | 50 |

- Outdoor Sensor Wireless transmission

- Transmission distance outdoor sensor 100 meter (open, barrier-free).

- send fast and accurate outdoor temperatures ℃/℉ and humidity (%RH).

- Min/max the record value.

- Outside room temperature range: -40 ℃ -+70℃ (-40℉ to 158 ℉) ; above 70 ℃ display HH.H, lower than -40 ℃ Show LL.L

- Outside room Humidity Range: 20-99% above 99% show HH, below 20% show LL

- Room the uses alkaline batteries outside.